## Slide 1
EVALUATING SCENARIOS THAT CAN STARTLE AND SURPRISE PILOTS
JENNIFER E. THROPP, Ph.D. ANDREW R. DATTEL, Ph.D.
COMMITTEE CHAIR COMMITTEE MEMBER
DONALD S. METSCHER, D.B.A. STEVEN HAMPTON, Ed.D.
MSA PROGRAM ADVISOR ASSOCIATE DEAN SCHOOL OF GRADUATE STUDIES
THESIS DEFENSE
RAHIM D. AGHA
EMBRY-RIDDLE
AERONAUTICAL UNIVERSITY
DAYTONA BEACH, FLORIDA
SCHOOL OF GRADUATE STUDIES, COLLEGE OF AVIATION

## Slide 2
INTRODUCTION
RESEARCH GAPS
PURPOSE STATEMENT
METHODOLOGY
RESULTS
DISCUSSION
PRACTICAL IMPLICATIONS
PRESENTATION OUTLINE
RECOMMENDATIONS

## Slide 3
BACKGROUND
The behavior of pilots in most Loss of Control-In Flight accidents is unexplained
    Pinnacle Airlines Flight 3701
    West Caribbean Airlines Flight 708
    Turkish Airlines 1951
    Air France 447
    Colgan Air 3407
An unexpected event on the flight deck can startle or surprise pilots based on the intensity
Startle and surprise are inherently different responses resulting from a different cause and effect
Surprise has been a factor in aviation accidents for the last three decades
Startle is a relatively new concept in aviation, which was talked about after CA3407 and AF447 accidents
Martin, Murray, and Bates (2012)
Federal Aviation Administration [FAA], 2017
National Transportation Safety Board [NTSB], 2010

## Slide 4
INTRODUCTION
Startle is defined as an uncontrollable and automatic muscle reflex, raised heart rate, and blood pressure elicited by exposure to a sudden, intense event that violates a pilot’s expectations
Surprise is defined as an unexpected event that violates a pilot’s expectations and can affect the mental processes used to respond to the event
Startle and Surprise on the Flight Deck
Pilots are accustomed to the idea that they will rarely face an emergency
So a quick transition from this presumed level of safety to a confusing (difficult) and life-threatening flight condition can startle and surprise pilots
Startle can impair ability to respond to a situation for 30 s to 1 min depending on the intensity of the situation
Surprise can also cause a significant delay in responding to an event
Federal Aviation Administration (2015)
Moriarty (2015)
Thackray and Touchstone (1970)

## Slide 5
RESEARCH GAPS
It is recommended to develop simulator scenarios that can startle or surprise pilots, and such scenarios to be used for training
However, a few studies have used startle and surprise interchangeably
    Using the terms interchangeably can lead to an only partial understanding of these constructs
To develop training scenarios, it is important to ascertain if the simulator scenario is startling, surprising, both, or neither
Presently, no study has evaluated workload during startle and surprise events
Gillen (2016)

## Slide 6
PURPOSE STATEMENT
To assess the differences in the physiological response and performance between startle and surprise conditions
    Heart rate (beats per minute) and respiration rate (breaths per minute) were recorded to validate if the scenario induced startle and surprise among pilots
The scenarios were compared for two aircraft (single-engine and multi-engine)
Pilots’ self-assessment of workload during startle and surprise events was recorded and evaluated using the National Aeronautics and Space Administration Task Load Index (NASA-TLX) [1 (Lowest) -20 (Highest)]

## Slide 7
METHODOLOGY
SAMPLE
DEPENDENT VARIBALES
RESEARCH DESIGN
INDEPENDENT VARIBALES
40 commercial pilots
(4 females)
Recruited using convince sampling
Experimental Design
2 x 3 within subjects
.
Aircraft
  Single-engine
  Multi-engine
Emergency Scenario
  Uninformed Surprise
  Uninformed Surprise and Startle
  Informed
Heart Rate
Respiration Rate
Mental Demand
Physical Demand
Temporal Demand
Subjective Performance
Effort
Frustration
*Flight performance was measured separately for each aircraft

## Slide 8
RESEARCH QUESTIONS
Do significant differences and interactions exist for heart rate and respiration rate based on the aircraft and emergency scenario?
Do significant differences and interactions exist for mental demand, physical demand, temporal demand, subjective performance, effort, and frustration based on the aircraft and emergency scenario?
Do significant differences exist in the flight performance among the emergency scenarios for the multi-engine aircraft as measured by altitude deviation?
Do significant differences exist in the flight performance among the emergency scenarios for the single-engine aircraft as measured by the number of engine-failure checklist steps followed?

## Slide 9
LIMITATIONS AND ASSUMPTIONS
The Aviation Training Device (ATD), though realistic in nature, involves simulation limits such as lack of motion and gravitational forces
Participants were not randomly selected for this study
Participant’s behavior was observed under controlled conditions, which may not be the same in a natural environment
Each participant was physically fit and capable of flying a scenario in an ATD
The participants have never received any training related to startle and surprise
The study also assumed construct validity in that the surprise and startle emergency properly reflected (or induced) startle and surprise

## Slide 10
EMERGENCY CONDITONS
Multi-Engine Aircraft

## Slide 11
EMERGENCY CONDITONS
Single-Engine Aircraft

## Slide 12
RESULTS
Manipulation Check
The participants were asked their perception of the simulator scenario flown with four possible answers; surprising, startling, both, or neither
Six chi-square goodness of fit tests were run to test the null hypotheses that participant perception for each emergency condition occurred with equal probabilities. All tests were significant (p < .001)
Variable | Multi-Engine |  |  |  | Single-Engine |  |  | 
 | Surprising | Startling | Both | Neither | Surprising | Startling | Both | Neither
Uninformed Surprise | 22 | 5 | 9 | 4 | 26 | 2 | 5 | 7
Uninformed Surprise and Startle | 8 | 9 | 20 | 3 | 10 | 8 | 20 | 2
Informed | 6 | 4 | 2 | 28 | 3 | 4 | 3 | 30

## Slide 13
RESULTS
Heart Rate and Respiration Rate
Heart Rate (HR)
Significant main effect for aircraft1(p = .005) and emergency condition1(p < .001), and significant interaction2(p = .040)
Respiration Rate (RR)
Significant main effect for aircraft1(p< .001) and emergency condition1(p < .001), and significant interaction2(p = .008)
Post Hoc Main Effect
HR and RR were significantly lower in the informed condition when compared to uninformed surprise and uninformed surprise and startle
HR and RR were highest in the uninformed surprise and startle condition
 | Multi-engine |  | Single-engine | 
 | M | SD | M | SD
Heart Rate1 |  |  |  | 
Uninformed Surprise | 82.33 | 9.94 | 79.59 | 8.27
Uninformed Surprise and Startle | 86.19 | 9.49 | 81.91 | 8.08
Informed | 79.54 | 8.42 | 77.63 | 7.54
Total | 82.69 | 8.78 | 79.71 | 7.43
Respiration Rate |  |  |  | 
Uninformed Surprise | 22.36 | 3.09 | 20.90 | 2.72
Uninformed Surprise and Startle | 23.72 | 3.18 | 21.44 | 2.83
Informed | 20.80 | 2.84 | 19.90 | 2.63
Total | 22.30 | 2.69 | 20.75 | 2.50
80.96
84.05
78.59
21.63
22.58
20.40
1large effect; 2medium effect

## Slide 14
RESULTS
Heart Rate and Respiration Rate
Post Hoc for Interaction
p < .001
p = .016
p = .001
p < .001

## Slide 15
RESULTS (NASA-TLX)
Mental and Physical Demand
Mental Demand (MD)
Significant main effect for aircraft1(p = .001) and emergency condition1(p < .001), and significant interaction2(p = .045)
Physical Demand (PD)
Significant main effect for aircraft1(p< .001) and emergency condition1(p < .001), and significant interaction2(p = .029)
Post Hoc Main Effect
MD and PD were significantly lower in the informed condition when compared to uninformed surprise and startle
MD and PD were highest in the uninformed surprise and startle condition
12.17
14.29
9.72
8.69
11.16
8.55
 | Multi-engine |  | Single-engine | 
 | M | SD | M | SD
Mental Demand |  |  |  | 
Uninformed Surprise | 13.27 | 4.69 | 11.08 | 4.50
Uninformed Surprise and Startle | 14.72 | 4.50 | 13.85 | 4.57
Informed | 11.15 | 4.63 | 8.30 | 4.64
Total | 13.05 | 4.17 | 11.07 | 4.02
Physical Demand |  |  |  | 
Uninformed Surprise | 9.33 | 4.42 | 8.05 | 4.81
Uninformed Surprise and Startle | 12.53 | 4.96 | 9.80 | 4.65
Informed Emergency | 10.05 | 5.05 | 7.05 | 4.72
Total | 10.63 | 4.46 | 8.30 | 4.43
1large effect; 2medium effect

## Slide 16
RESULTS (NASA-TLX)
Mental and Physical Demand
Post Hoc for Interaction
p = .002
p = .003
p < .001
p < .001

## Slide 17
RESULTS (NASA-TLX)
Temporal Demand and Subjective Performance
Temporal Demand (TD)
Significant main effect for aircraft1 (p < .001) and emergency condition1(p < .001), and significant interaction1(p < .001)
Subjective Performance (SP)
Significant main effect for aircraft1(p< .001) and emergency condition2(p < .001), and significant interaction (p = .029)
Post Hoc Main Effect
TD and SP were significantly lower in the informed condition when compared to uninformed surprise and startle and uninformed surprise condition
TD and SP were highest in the uninformed surprise and startle condition
 | Multi-engine |  | Single-engine | 
 | M | SD | M | SD
Temporal Demand |  |  |  | 
Uninformed Surprise | 13.58 | 4.73 | 8.22 | 5.07
Uninformed Surprise and Startle | 13.43 | 5.12 | 12.83 | 4.68
Informed | 10.45 | 5.07 | 7.90 | 4.78
Total | 12.48 | 4.27 | 9.65 | 4.04
Subjective Performance |  |  |  | 
Uninformed Surprise | 15.20 | 4.78 | 13.03 | 4.91
Uninformed Surprise and Startle | 16.70 | 3.90 | 14.33 | 3.85
Informed | 11.98 | 5.08 | 6.67 | 4.45
Total | 14.63 | 3.19 | 11.34 | 3.29
10.90
13.12
9.17
14.11
15.51
9.32
1large effect; 2medium effect

## Slide 18
RESULTS (NASA-TLX)
Temporal Demand and Subjective Performance
Post Hoc for Interaction
p = .013
p < .001
p < .001
p = .003

## Slide 19
RESULTS (NASA-TLX)
Effort and Frustration
Effort
Significant main effect for aircraft1(p < .001) and emergency condition1(p < .001), and no significant interaction (p > .050)
Frustration
Significant main effect for aircraft1(p< .001) and emergency condition1(p < .001), and no significant interaction (p > .050)
Post Hoc Main Effect
Effort and frustration were significantly lower in the informed condition when compared to uninformed surprise and startle and uninformed surprise condition
Effort and frustration were highest in the uninformed surprise and startle condition
 | Multi-engine |  | Single-engine | 
 | M | SD | M | SD
Effort |  |  |  | 
Uninformed Surprise | 12.70 | 4.40 | 10.67 | 4.42
Uninformed Surprise and Startle | 15.28 | 4.37 | 12.67 | 4.53
Informed Emergency | 11.67 | 3.93 | 9.15 | 4.43
Total | 13.22 | 3.35 | 10.83 | 3.88
Frustration |  |  |  | 
Uninformed Surprise | 13.15 | 5.33 | 9.75 | 5.67
Uninformed Surprise and Startle | 14.78 | 5.45 | 12.18 | 5.50
Informed | 70.23 | 5.28 | 7.03 | 4.65
Total | 12.72 | 4.70 | 9.65 | 4.51
11.69
13.97
10.41
11.45
13.47
8.62
1large effect; 2medium effect

## Slide 20
RESULTS (FLIGHT PERFORMANCE)
Multi-Engine Aircraft
Altitude deviation between the emergencies significantly varied, F(2, 78) = 67.34, p < .001, η2 = .63 (large effect size)
Altitude deviation was the highest in the uninformed surprise and startle condition, and lowest in the informed emergency condition
Single-Engine Aircraft
Number of engine failure checklist steps followed significantly varied,
F(2, 78) = 106.10, p < .001, η2 = .73 (large effect size)
Checklist compliance was the lowest in the uninformed surprise and startle condition, and highest in the informed emergency condition

## Slide 21
DISCUSSION
Heart Rate and Respiration Rate
RR was higher for an uninformed surprise emergency compared to an informed emergency, which was consistent with Bruna, Levora, and Holub (2018)
HR was also higher for uninformed surprise emergency compared to an informed emergency
However, HR and RR will be the highest for a multi-engine aircraft if startle comes in conjunction with uninformed surprise emergency
HR and RR were similar for the different aircraft while flying the informed emergency condition

## Slide 22
DISCUSSION
Mental Demand, Physical Demand, and Temporal Demand
MD, PD, and TD were higher for the multi-engine aircraft
Flying a multi-engine aircraft for an uninformed surprise and startle condition was associated with higher MD and PD
TD was highest for the uninformed surprise condition
MD and TD were not different between the aircraft for the uninformed surprise and startle condition
It can be argued that the initial behavioral response to fear would not vary with respect to whether the pilot is flying a single- or multi-engine aircraft

## Slide 23
DISCUSSION
Subjective Performance (SP), Effort, and Frustration
Most participants rated their SP as not up to their own standards except for the informed condition
SP was highest (not good) in the uninformed surprise and startle condition for the multi-engine aircraft
Effort had no significant interaction; it was one of those cases where the difference was just not statistically significant
Consistent with most results, effort and frustration were the highest in the uninformed surprise and startle condition for the multi-engine aircraft

## Slide 24
DISCUSSION
Flight Performance
Performance was better in the informed conditions for both aircraft
Twenty-two participants crashed the multi-engine aircraft in the uninformed surprise and startle condition
  “I was trying to find the runway and did not monitor my instruments for 10 to 15 s” per one participant flying the uninformed surprise condition
Checklist steps were missed the most in the uninformed surprise and startle emergency
Engine failure training should incorporate startle and surprise as a factor

## Slide 25
PRACTICAL IMPLICATION
The simulator scenarios proposed in this study can be potentially be used for startle and surprise training for commercial pilots
Heart rate and respiration rate can be used as a physiological measurement for startle and surprise
Startle and surprise are not interchangeable terms in the aviation industry, and it is important that the research fraternity recognizes this difference
Aircraft type could be a factor during startle and surprise events
Workload is affected during startle and surprise events and can potentially have adverse effects on flight crew

## Slide 26
2
Flying an informed emergency condition is predictable and the training potentially does not transfer to actual emergency situations
Flight Performance
HR and RR can be used as physiological markers to ascertain if a flight simulator scenario was surprising or startling
Heart and Respiration Rate
1
CONCLUSON
For commercial pilots, the type of aircraft they are flying can impact their performance, vital signs (HR and RR), and workload during surprising and startling events. The key result of this study highlighted that having pilots solely fly informed emergency scenarios in training is inadequate because it might make the training predictable; something with which Bhana (2010) agreed.
3
Startle and surprise can negatively effect workload, and can be higher for a multi-engine aircraft
Workload

## Slide 27
2
A sample of 40 would give the future researchers an adequate power (.80) if they want to investigate the effects of startle and surprise on aircraft and emergency
Sample Size
Future studies should focus on validating electroencephalography and electromyography as measures for startle and surprise
Vital Signs
1
RECOMMENDATIONS
3
Use the NASA-TLX or other mechanisms to evaluate pilot workload during startle and surprise events
Workload

## Slide 28
THANK YOU
Contact
Rahim Agha
aghar@my.erau.edu

## Slide 29
REFERENCES
Bhana, H. (2010). Correlating boredom proneness and automation complacency in modern airline pilots. Collegiate Aviation Review, 28(1), 9–24. Retrieved from http://search.proquest.com.ezproxy.libproxy.db.erau.edu/docview/859874566?accountid=27203
Bruna, O., Levora, T., & Holub, J. (2018). Assessment of ECG and respiration recordings from simulated emergency
landings of ultra light aircraft. Scientific Reports, 8(1), 7232-10. doi:10.1038/s41598-018-25528-z
Federal Aviation Administration (2015). Stall Prevention and Recovery Training. (FAA-AC: 120-109A). Washington, DC: U.S. Department of Transportation. Retrieved from https://www.faa.gov/documentLibrary/media/Advisory_Circular/AC_120-109A.pdf
Federal Aviation Administration (2017). Upset Prevention and Recovery Training (FAA-AC: 120-111). Washington, DC: U.S. Department of Transportation. Retrieved from https://www.faa.gov/documentLibrary/media/Advisory_Circular/AC_120-111_CHG_1.pdf
Gillen, M. W. (2016). A study evaluating if targeted training for startle effect can improve pilot reactions in handling
unexpected situations in a flight simulator (Doctoral dissertation). Retrieved from http://huntlibrary.erau.edu/

## Slide 30
REFERENCES
Martin, W. L., Murray, P. S., & Bates, P. R. (2012). The effects of startle on pilots during critical events: A case study analysis. Proceedings of 30th EAAP Conference: Aviation Psychology & Applied Human Factors. 387–394. Retrieved from https://research-repository.griffith.edu.au/bitstream/handle/
10072/54072/82496_1.pdf?sequence=1
Moriarty, D. C. (2015). Practical human factors for pilots. Retrieved from https://ebookcentral.proquest.com
National Transportation Safety Board. (2010). Aircraft Accident Report (NTSB/AAR-10/01). Retrieved from https://www.ntsb.gov/investigations/AccidentReports/Reports/AAR1001.pdf
Thackray, R., & Touchstone, R. M. (1970). Recovery of motor performance following startle. Perceptual Motor Skills, 30, 279-292. https://doi.org/10.2466/pms.1970.30.1.279