## Slide 1: Where is Space? And Why Does That Matter?
Bhavya Lal, Ph.D. Research Staff Member Emily Nightingale, Science Policy Fellow
Science and Technology Policy Institute, 1899 Pennsylvania Avenue NW, Washington DC 20006
November 5, 2014

## Slide 2: Agenda
Why is this an important question?
What are some technical answers?
Why have we not wanted to answer the question?
Has anything changed since we last visited the question?

## Slide 3: Some technical answers

## Slide 4: 50 mi (80 km)?
Roughly the point at which aerodynamic control surfaces are no longer useful
Set through testing of the X-15
Notes: Talk to Dr. Lewis for entire story again

## Slide 5: 62.5 mi (100 km)?
Karman line - A vehicle at this point (which can be between 53-60 mi depending on air density) would have to fly faster than orbital velocity to derive sufficient aerodynamic lift from the atmosphere to support itself.
As certain parameters, such as solar flux, magnetic index, and others are varied, the calculated altitude varies.
However, the boundary to space is set at 100 km for ease of use.
This is the most common and internationally used boundary, and was also the target altitude used by the Ansari X-Prize to build and launch a “spacecraft”
Notes: Atmosphere becomes too thin at around this altitude to support aerodynamic flight; the vehicle needs to exceed orbital velocity to have sufficient aerodynamic lift.

## Slide 6: 73 mi (118 km)?
The midpoint of gradual transition over tens of kilometers from relatively gentle winds of the Earth’s atmosphere to more violent flows of charged particles in space.
As found with the Supra-Thermal Ion Imager measuring ion collision frequency and ion cyclotron frequency
  Study examined space between 100km and 150 km.
  There is a gradual transition from magnetospheric to thermospheric control.
  This area is important because it affects the transition of an object from aeronautic to astronautic flight control.
  Found by Sangelli et Al., but not functionally used by an organization

## Slide 7: 76 mi (122 km)?
Boundary used by NASA Mission Control as the point of reentry and at which atmospheric drag becomes noticeable.
There is not one single point at which atmospheric drag because noticeable because it depends on the object
NASA uses this demarcation because it is the altitude at which the shuttle changed from astronautical control with thrusters to aeronautical control via air surfaces.

## Slide 8: 80-93 mi (129-150 km)?
The US Army training documents refer to the 80-93 miles zones as the lowest perigee attainable by an orbiting space vehicle.
80 miles is the lowest altitude at which an object in an elliptical orbit can complete at least one full revolution without propulsion and 93 miles is the lowest orbit an object in circular orbit can complete one full revolution.
The lowest recorded orbit for a satellite was the Compton Gamma Ray Observatory that orbited the Earth one last time before reentry at a perigee of 93 miles in 1999.
However this perigee is not sustainable for more than one full orbit around Earth (Harwood 2000). This orbit is unsustainable. In fact, it is not until 200 miles that an object can orbit without propulsion and not reenter Earth’s atmosphere (Army Space Reference Text).

## Slide 9: Summary of Demarcation Altitudes
Notes: 5 different definitions used by different groups and organizations around the world. Each has merit, but it is clear that there is not one outstanding definition. Right now each definition is measured through: air/space craft maneuvering (50miles with X15 and Shuttle at 76 miles and 80-93 mile zones for the lowest perigee (we can assume that the calculations were made using a specific assumption about the object mass/ size). Therefore each of these definitions could change with a different object. Two final definitions remain: the Karman line and the midpoint of space winds. The midpoint of space winds is interesting, but it is only one of the changes in space: you could use different measurements to achieve new lines of delimitation. Finally, the Karman line changes depending on the days solar flux or magnetic index.

## Slide 10: Typical Arguments For and Against Having a Delimitation

## Slide 11: Typical Arguments Against Having a Delimitation
The United Nations General Assembly Outer Space Treaty does not specify a starting point for space.
There have not yet been adverse effects of not having one
  There is fear of preemptively creating an arbitrarily definition which could later hinder the use of a new technology.
  Imprecision in definitions

## Slide 12: Typical Arguments For a Delimitation
Passage into Foreign Air Space
  The BRAUN satellite in 1988 and the U.S. Space Shuttle flew under 110 km altitude during landing (Benko 2013).
  In 2012 South Korea threatened to shoot down a North Korean satellite if it entered South Korea’s air space.
Sohae Satellite Launching Station Location

## Slide 13: Typical Arguments For a Delimitation
Innocent passage
  A term that refers to maritime concept that grants a foreign nation access to territorial waters when the vessel is peaceful.
  What if a nation claims non-innocent passage? (Ito 2011)

## Slide 14: Emerging Arguments for Considering Delimitation
Increasing international participation

## Slide 15: Increasing Sub-Orbital Traffic
Chart: Suborbital Vehicles
| World View (Balloon) | X-15 | Hyperion | New Shepard | Xaero | SpaceShipTwo | Lynx | SpaceLiner | Swiss Space Systems | SpaceLoft | ARCASPACE
Altitude (miles) | 18.6 | 50 | 62.5 | 62.5 | 62.5 | 62.5 | 62.5 | 62.5 | 62.5 | 99.5 | 112

## Slide 16: Summary
Arguments against delimitation follow the line of reasoning that a lack of definition has not hurt space developments, and therefore no standardized definition is necessary.
Arguments for delimitation are related to international disputes regarding crossing perceived airspace
There are emerging arguments for delimitation that must be examined carefully
  Increasing international participation in space activities
  Increasing sub-orbital traffic
Do we need to revisit the question more carefully?